Trusted Path
- Intercept data in transit
- Optionally store and analyze later
- Principle idea behind key logger, and other eavesdropping techniques
- A number of steps in the transmission path need to be trusted:
Keys typed → Interpreted by keyboard micro-controller → Transmitted on PS/2 bus → Interpreted by host keyboard controller → Interpreted by Operating System
Works at the Transmitted on PS/2 bus step

---
Implementation
- PS/2 is a serial protocol; each byte is sent one bit at a time:
- Two wires in transmission: clock and data
- Signaling at ~20-30khz

---
Which key was pressed? Scancodes
- Two types: commands, keystrokes
- Commands tell host, or keyboard to do something, e.g. turn lights on, resend data, etc.
- When key is pressed, keyboard sends “make” code, when released, sends “break” code
- The whole sequence is typically 3 bytes
- How many can we store:
  - Design is spec'd for 1024 bytes, 1024/3 ~= 341
  - This data could be coded down easily to have 1:1
  - A larger EEPROM can be purchased

---
Bill of Materials
- Microchip 16F883 PIC Micro-controller “the brains”, $3.92
- Microchip 24AA08 8kbit serial EEPROM “the memory”, $0.57
- Various standard electronic bits.

---
Demo!

---
If we have time...
- Real world cases: FBI has used for cracking encryption and email for alleged drug case, mobster
- What if manufacturers are required to install such a system? (All your keystrokes are belong to us)
- Attack variations:
  - Modifying the keyboard directly
  - Wireless eavesdropping, TEMPEST attack

---
Defense
- Annoying and dubious:
  - screen keyboard
  - epoxied keyboard (once it is secured)
  - checking cable

---
Questions?